INSTRUCTION MANUAL- 54LED SOLAR FLOODLIGHT

www.metrosolarmatics.com

IN THE BOX:

● Light Fixture w/ Built In Battery & Charging Circuit

● Solar Panel (11.5” x 13.5” x 0.5”)

● Solar Panel & 10’/3m Light Fixture Wiring

Technical Specs.: Model SP-0011 54 LED FLOODLIGHT

Solar Panel: 17V/10W; 335x280x17mm; Weight: 2.1kg;

Rechargeable Lead Acid Battery: 12V/4Ah

Rated Output Voltage 12V DC

Rated Output (Fully Charged) 40Wh

Maximum Output 48Wh

LED: 54pcs/2.5W

Light Run Time (Fully Charged): 6 to10 hrs+ ;

Intelligent controller: Overcharge/discharge controller;

Light unit dimensions: 280x210x170mm: Weight: 3.5kg;

Gross weight: 5.1kg;

System Weight 12.31 Lbs

Operating Instructions:

1. Mount the light fixture in your desired location using the metal bracket

with holes in it as the support bracket. This bracket can be used as a stand and placed or bolted directly to the ground, to your house or post. Adjust tilt and tighten bolts on the fixture where the bracket meets it.

2. Find suitable area to place solar panel in full sunlight without shadows crossing the panel within the wire length from the panel to the fixture. Aluminum frame of panel is drillable to allow you to customize your own mounting. It is recommended to place the panel at a 45 degree angle towards the sun for maximum solar gain.

Note: Do not drill through the glass that recedes into the framing of the panel.

3. Connect white adapter piece on the wire from the panel to the corresponding adapter from the light fixture.

4. Be sure fixture switch is in the “on” position, indicated by a Straight line (I), and charge for at least 8 hrs in full sun exposure (switch MUST be in

the ON position in order for the battery to charge). After this point the light will automatically turn on at night and turn off at dawn (light will only come on at night).

Battery Replacement:

1. With a Phillips head screwdriver take out the four screws① that hold the back housing② onto the light.

2. Take off back housing gently and softly to avoid damaging the wires.

3. Unscrew the two screws③ and remove the strap④ that hold the battery down.

4. Disconnect the battery wires from positive and negative terminals of the battery.

5. Remove the old battery.

6. Replace with new battery of same kind and capacity.

7. Screw the strap back down with one Phillips head screw.

8. Connect the battery wires to the new battery being sure they go to the correct polarities.

9. Then screw back cover on tightly with the other four screws being sure the water seal is seated correctly.

The LEAD-ACID battery included with this product is rechargeable. Like all rechargeable batteries, however, it will eventually need to be replaced. If the light should begin to illuminate dimly or stays on for shorter duration of time, you should replace it.

Maintenance:

DISCONNECT THE SOLAR PANEL FROM THE LIGHT IF YOU PLAN TO STORE THE UNIT FOR A PROLONGED PERIOD OF TIME. To maximize battery life, unit must be charged once or twice a month when not in use.